## Slide 1
SIMULATION STUDY
XtraFlow
Fuel-weighted traffic signals
A locked comparison on mixed Indian traffic. Same demand, 8 controllers, 4 demand patterns. Not a field deployment. Live demos: SUMO side-by-side + YOLO camera clips.
4
scenarios
5
test seeds, scored once
2
live clips to play
github.com/couder-04/XtraFlow
Simulation-based estimate; assumed traffic mix
Notes: Open on energy, not on travel time. Say out loud that this is a simulation before the first percentage. Scope: 5 test seeds (1–5). Source label: Simulation-based estimate; assumed traffic mix. Demo order later: results/demo/demo.mp4, then results/demo/yolo/yolo_story.mp4.

## Slide 2
TALK MAP
What you will see
Numbers first from the locked TEST. Clips last — they illustrate, they do not replace the headline.
XtraFlow · Simulation-based estimate
02
01
Idea
Adaptive pressure vs fixed timing; fuel weights are a small add-on.
02
Locked TEST
Same demand, fair baselines, full figure gallery on disk.
03
Live · SUMO
Side-by-side: fixed timing vs XtraFlow on one seed.
04
Live · YOLO
Camera mosaic with GO/WAIT story, then per-cam overlays if asked.
05
Limits
Detection miss, unscored grid, oracle TEST, next field steps.
Notes: Skip nothing in 01–03 for a short talk. Play both live clips. Robustness / grid / scaling are backup if asked.

## Slide 3
THE PROBLEM
A stopped queue is burning fuel
Fixed green cannot see which approach is waiting, or what that wait costs.
XtraFlow · Simulation-based estimate
03
01
Fixed green is blind
The split stays put when one road is empty and the other is full. Webster helps the average hour. It still lags a peak that moves.
02
A count is the wrong unit
Here a truck idles at 2.8× a car, a two-wheeler at 0.54×. Treating them as one vehicle spends green on the wrong queue.
03
The question
If the signal weighs each vehicle by idle fuel, do fuel, CO₂, delay, and queues fall — inside hard green, yellow, and all-red limits?
LEFT-HAND TRAFFIC · ONE FOUR-ARM JUNCTION
Assumed mix · two-wheelers 40% · cars 30% · trucks 15% · autos 10% · buses 5%
Notes: The mix is assumed until observed counts are supplied. Do not present it as a city survey. Idle-fuel ratios are measured in SUMO, not guessed.

## Slide 4
THE CONTROLLER
Weigh the queue by the fuel it burns
Idle-fuel weights are a small add-on on top of adaptive pressure (about 0–2% vs count-only on TEST).
XtraFlow · Simulation-based estimate
04
Weights come from a 60-second probe of fuel burned while the vehicle is stopped. Emission classes are assumed. Autos and cars share a class in this run, so they share a weight.
Chosen on validation only
Look back 150 m. Count moving vehicles at 0.50. Switch only past hysteresis 0.25. Scenario: .
Two-wheeler
0.54×
Auto
1.00×
Car
1.00×
Bus
2.00×
Truck
2.77×
TIMING THAT STAYS IN FORCE
15 s
Min green
90 s
Max green
3 s
Yellow
2 s
All-red
120 s
Must serve
Notes: Explain hysteresis: the new phase must beat the current pressure by the tuned margin. Must-serve forces a switch so a waiting approach is not ignored. Weights file: results/weights.json. Tuned parameters: results/tuned_params.json, validation seeds only.

## Slide 5
HOW A DECISION IS MADE
See the queue. Score the fuel. Keep the timing.
The signal never skips yellow or all-red, and it cannot hold green past the cap.
XtraFlow · Simulation-based estimate
05
01
See
Detectors on each approach, or a camera. A YOLO overlay demo is on a later slide — input feasibility, not a fuel-saving result. Locked TEST scores still use the oracle detector; detector-miss noise for robustness stays assumed (15% in the smoke check).
02
Score
Each queued vehicle is scaled by its idle-fuel weight. Moving vehicles count at the tuned fraction. The phase changes only after minimum green, and only if the gain clears hysteresis.
03
Measure
Fuel and CO₂ come from SUMO on every completed trip. Waiting and queues use the same seed the other controllers saw. The test set was not used to pick the settings.
Notes: Play the YOLO story after the side-by-side SUMO demo (yolo_story.mp4). Say clearly: YOLO is input feasibility; headline fuel numbers are oracle TEST. Do not claim a field detector result.

## Slide 6
THE EXPERIMENT
Same cars for every controller
Settings are frozen before the test. 5 test seeds (1–5). A seed is one hour of the same demand, replayed.
XtraFlow · Simulation-based estimate
06
TRAIN
1000 – 1049
Reinforcement-learning baseline only
VALIDATION
2000 – 2019
Settings chosen here, then frozen
TEST
1 – 5
5 locked seeds in raw_runs.csv
Low demand
150 veh/h on every approach.
Shifting
The heavy axis swaps every 20 min. 680 against 200 veh/h.
Peak, one-sided
North–south 720 veh/h. East–west 180.
Balanced
480 veh/h on every approach.
Compared with Fixed time, Tuned fixed, Webster, Actuated, Queue pressure, Max-pressure, Count only. PPO was trained to the config budget and is not in this TEST table.
Sublane probe used. Full-demand stability under that setting is not re-claimed here.
Notes: Same seed means identical demand. Test seeds are the ones stored in results/raw_runs.csv. Sublane use is the used_sublane field in results/sublane_fallback.json. RL note: Time cut. This zip is the 200000-step model. It was not scored on VALIDATION or TEST, so rl_ppo is not in raw_runs.csv.

## Slide 7
TEST SET
Small edge vs the strongest baseline (0.3–1.9%)
Fuel vs best tuned baseline is only 0.3–1.9% (5 paired seeds; Holm p=1). Large cuts are vs fixed / Webster / actuated, not class fuel weights.
XtraFlow · Simulation-based estimate
07
Low demand
1.9%
0.5 – 3.0
vs Max-pressure
vs legacy fixed 14.1%
Shifting
1.1%
0.6 – 1.7
vs Max-pressure
vs legacy fixed 13.2%
Peak, one-sided
0.7%
-0.4 – 1.8
vs Max-pressure
vs legacy fixed 17.5%
Balanced
0.3%
-0.4 – 1.0
vs Max-pressure
vs legacy fixed 7.9%
Mean fuel is lower than the best baseline in every scenario. Some 95% intervals still cross zero — read the interval, not only the point estimate.
Notes: Primary headline vs best of fixed_tuned / actuated / queue_pressure / maxpressure is only 0.3–1.9% (n=5; Holm p=1). The 8–17% cuts are vs fixed / Webster / actuated. Published maxpressure ≡ queue_pressure (downstream was ~0); re-run after occupancy fix. Numbers are from results/headlines.json.

## Slide 8
THE HONEST COMPARISON
Versus strong adaptive controllers, the edge is small
Against max-pressure / queue_pressure the cut is 0.3–1.9% (and those two matched bit-for-bit in this publish). Legacy fixed is the easy win.
XtraFlow · Simulation-based estimate
08
Scenario
vs legacy fixed
vs tuned fixed
vs actuated
vs max-pressure
Low demand
14.1%
12.7 – 15.5
12.1%
11.4 – 12.8
10.7%
9.0 – 12.4
1.9%
0.5 – 3.0
Shifting
13.2%
12.3 – 14.3
17.0%
15.1 – 18.9
8.5%
7.8 – 9.2
1.1%
0.6 – 1.7
Peak, one-sided
17.5%
14.4 – 20.3
9.6%
8.0 – 11.2
8.5%
6.6 – 10.0
0.7%
-0.4 – 1.8
Balanced
7.9%
6.7 – 9.1
7.6%
6.7 – 8.4
4.8%
4.3 – 5.3
0.3%
-0.4 – 1.0
Versus max-pressure: 0.3% to 1.9%. Some intervals still cross zero. Versus the count-only ablation: 0.1% to 2.0%. PPO is trained but not scored in this TEST table.
Notes: Read the paired intervals on this slide from the loaded comparison table. Do not add a verdict that is not in those intervals. RL is a baseline trained with the budget in rl_selection.json.

## Slide 9
WHAT CHANGES
Shorter waits, shorter queues, less CO₂
Peak, one-sided on the locked test. Completed trips match fixed time (1,801).
XtraFlow · Simulation-based estimate
09
FUEL / VEHICLE
0.151 L
0.125 L
from fixed time
MEAN WAIT
37.0 s
18.4 s
from fixed time
MEAN QUEUE
17.5 veh
9.0 veh
from fixed time
CO₂
679 kg
560 kg
from fixed time
WAITING TIME ON THE OTHER SCENARIOS
Low demand
27.2 s to 16.2 s
41% shorter
Shifting
32.2 s to 18.8 s
42% shorter
Balanced
30.0 s to 21.8 s
27% shorter
Notes: Levels are means from results/tables/summary_mean_std.csv. The fuel percentage on the previous slide is the mean of paired percent cuts, which is not identical to the percent gap between these two means. Waiting cuts are percent gaps between means. Say that if someone mixes the two.

## Slide 10
FIGURES
Metrics by controller · Fuel cut vs baselines
Regenerated from results/ by analyze.py and the study scripts.
XtraFlow · Simulation-based estimate
10
METRICS BY CONTROLLER
Fuel, CO₂, wait, and queue (mean±std)
FUEL CUT VS BASELINES
Paired % reduction versus tuned baselines
Notes: PNGs live in results/figures/. Do not describe a trend that is not visible in the figure. RL / grid / extrapolation slides inherit the same caveats as STATE.md.

## Slide 11
FIGURES
Dynamic queue series · Green allocation
Regenerated from results/ by analyze.py and the study scripts.
XtraFlow · Simulation-based estimate
11
DYNAMIC QUEUE SERIES
Queue time series on the dynamic scenario
GREEN ALLOCATION
XtraFlow green share versus fixed timing
Notes: PNGs live in results/figures/. Do not describe a trend that is not visible in the figure. RL / grid / extrapolation slides inherit the same caveats as STATE.md.

## Slide 12
FIGURES
Fuel by vehicle type · Gain vs saturation
Regenerated from results/ by analyze.py and the study scripts.
XtraFlow · Simulation-based estimate
12
FUEL BY VEHICLE TYPE
Mean fuel split across the assumed mix
GAIN VS SATURATION
Fuel gain vs demand multiplier proxy (sensitivity data; re-run pending)
Notes: PNGs live in results/figures/. Do not describe a trend that is not visible in the figure. RL / grid / extrapolation slides inherit the same caveats as STATE.md.

## Slide 13
FIGURES
Detection-miss robustness · RL training
Regenerated from results/ by analyze.py and the study scripts.
XtraFlow · Simulation-based estimate
13
DETECTION-MISS ROBUSTNESS
Fuel under rising detector miss rates
RL TRAINING
PPO training curve (unscored on TEST)
Notes: PNGs live in results/figures/. Do not describe a trend that is not visible in the figure. RL / grid / extrapolation slides inherit the same caveats as STATE.md.

## Slide 14
FIGURES
Emission cross-check · 2×2 grid
Regenerated from results/ by analyze.py and the study scripts.
XtraFlow · Simulation-based estimate
14
EMISSION CROSS-CHECK
Primary vs alternate emission classes
2×2 GRID
Grid sweep (unscored TLS caveat applies)
Notes: PNGs live in results/figures/. Do not describe a trend that is not visible in the figure. RL / grid / extrapolation slides inherit the same caveats as STATE.md.

## Slide 15
FIGURES
Extrapolation · Phase choice sketch
Regenerated from results/ by analyze.py and the study scripts.
XtraFlow · Simulation-based estimate
15
EXTRAPOLATION
Placeholder scaled fuel / INR range
PHASE CHOICE SKETCH
How fuel-weighted pressure picks a phase
Notes: PNGs live in results/figures/. Do not describe a trend that is not visible in the figure. RL / grid / extrapolation slides inherit the same caveats as STATE.md.

## Slide 16
LIVE CLIP 1 · CONTROL
Fixed timing on the left. XtraFlow on the right.
One seed, same arrivals. Qualitative demo — the fuel numbers are on the previous slides.
XtraFlow · Simulation-based estimate
16
PLAY NOW
results/demo/demo.mp4
Open the file in a video player beside the deck. Same demand seed: legacy fixed versus XtraFlow. Do not treat the clip as a percentage claim.
Next: YOLO story clip — GO/WAIT on four cameras.
WHAT TO SAY
1. Same cars on both sides.
2. Left is fixed green.
3. Right is fuel-weighted pressure.
4. Watch which approach gets green when the queue is heavy.
Notes: Open results/demo/demo.mp4 (or demo.gif) while presenting. Then advance to the YOLO story slide and play yolo_story.mp4. Say that the SUMO demo is qualitative; the headline numbers are on the previous slides.

## Slide 17
LIVE CLIP 2 · PERCEPTION
YOLO story video — click to play in PowerPoint
Input feasibility — not a fuel-saving result
XtraFlow · Simulation-based estimate
17
CLICK VIDEO TO PLAY
Embedded on this slide.
results/demo/yolo/yolo_story.mp4
1. Green = that axis moves. Red = wait.
2. Phase picks the highest fuel-weighted pressure.
3. Four independent corridor cams — not one junction.
4. Not the locked SUMO fuel headline.
CLIP STATS (PROXY — NOT TEST)
mean ~15 veh across cams · peak 24 · idle-fuel proxy vs fixed 22% on this clip only
Notes: Click the embedded yolo_story.mp4 on this slide to play in PowerPoint (Slideshow or Normal view). Say: GO/WAIT is illustrative from detector counts; published fuel is oracle SUMO TEST. Next slide has mosaic + per-cam overlays if you want to linger.

## Slide 18
LIVE CLIP 2B · OPTIONAL
Mosaic and per-camera overlays
Play if someone asks how each approach looks. Same caveat: input feasibility only.
XtraFlow · Simulation-based estimate
18
N · Straight multi-lane (Zenodo cam_10)
E · Straight street (Zenodo cam_16)
S · I-5 S @ 188th St (WSDOT)
W · Divided arterial (Zenodo cam_11)
PLAY THESE
● Mosaic (2×2)
results/demo/yolo/yolo_mosaic.mp4
● Primary overlay
results/demo/yolo_overlay.mp4
● Cam N
results/demo/yolo/overlay_N.mp4
● Cam E
results/demo/yolo/overlay_E.mp4
● Cam S
results/demo/yolo/overlay_S.mp4
● Cam W
results/demo/yolo/overlay_W.mp4
ATTRIBUTION
Four independent corridor cameras mapped to N/E/S/W for a mosaic. Not synchronized approaches of one intersection. S is true southbound one-way highway; N/E/W are Zenodo arterial cams.
Mixed research CCTV — straight / one-way corridors · Zenodo DOI 10.5281/zenodo.3986141 (CC BY 4.0); Seattle I-5 trafficdb (WSDOT / Chan–Vasconcelos)
Notes: Optional. Prefer yolo_story on the previous slide for the talk. Use mosaic or one overlay only if asked. Do not claim a synchronized field site.

## Slide 19
IF THE CAMERA MISSES
At the highest miss rate, mean fuel is under the reference lines
Peak, one-sided. 3 seeds. Vehicles are dropped from the detector at random.
XtraFlow · Simulation-based estimate
19
0% missed
0.123
litres / vehicle
± 0.002 · n=3
10% missed
0.123
litres / vehicle
± 0.002 · n=3
20% missed
0.124
litres / vehicle
± 0.001 · n=3
30% missed
0.124
litres / vehicle
± 0.001 · n=3
SAME SEEDS, NO MISSES
0.123 L
XtraFlow
0.136 L
Actuated
Every miss level on this slide has lower mean fuel than every reference line. Noise-model point (see noise_model.json) is 0.125 L.
Notes: Means are grouped from results/robustness.json. Do not describe the curve as flat unless the loaded means say so. The noise-model source field is empirical only when labels exist.

## Slide 20
WHERE IT DOES NOT TRANSFER
The 2×2 grid was not scored in this publish
A corridor result is only quoted from results/grid_results.json after a successful sweep.
XtraFlow · Simulation-based estimate
20
NO NUMERIC GRID CLAIM
2x2 grid not scored in this time-cut run. duarouter path was fixed, but the single-intersection tls.add.xml does not provide programs for the grid TLS ids, so SUMO aborts.
Do not scale the single-junction result to a city.
Notes: Read results/grid_results.json. If rows and summary_means are empty, say the grid was not scored. Label: simulation-based estimate; assumed traffic mix.

## Slide 21
BESIDE THE HEADLINE
Safety: mixed. Emissions: Intervals overlap.
Both lines are the verdict fields in the loaded JSON, not a fixed sentence.
XtraFlow · Simulation-based estimate
21
SAFETY
Mixed
Time-to-collision conflicts from the simulator. Verdict vs fixed only; vs max-pressure/queue-pressure the CI includes 0; vs count-only (ours_count) XtraFlow shows MORE conflicts. A model count, not a crash record.
EMISSIONS MODEL
Intervals overlap
Primary model 13.9%. Alternate model 13.7%. The reduction shrinks. It does not flip.
PERCEPTION
YOLO demo ready
Camera overlays exist under results/demo/yolo/. They are input feasibility only. Locked TEST fuel still uses the oracle detector. Robustness miss rates remain assumed until labeled video replaces the noise model.
Notes: Safety verdict comes from results/safety.json. Emission cross-check is HBEFA3 versus PHEMlight on a smaller seed set than the main test; quote both percentages. YOLO demo does not replace the oracle TEST claim.

## Slide 22
SCALING
Per vehicle is measured. Per year is a range.
Illustrative only: built from a 0.3–1.9% gap whose CIs include 0 on 2 of 4 scenarios (n=5). Not a forecast.
XtraFlow · Simulation-based estimate
22
MEASURED VS BEST BASELINE (SCENARIO-WEIGHTED)
0.001 L saved / vehicle
5th – 95th percentile of that mean: 0.001 – 0.002 L
IF THAT SAVING IS MULTIPLIED OUT
0.3 million litres
2.7 million litres
0.9 million litres
median of the scaled draws
CO₂ median 2,296 tonnes · 629 tonnes – 6,640 tonnes
Why the bar is wide
Junctions
50 – 1,000
Vehicles / peak hour
800 – 2,200
Peak hours / day
3 – 7
Days / year
250 – 330
Rupee value uses a placeholder price, so it is not shown.
Notes: Lead with the per-vehicle litres. The annual figure multiplies that saving by the ranges on the right, Monte Carlo from config.yaml. The price in fuel.price_inr_per_L is a placeholder. Quote the extrapolation label: simulation-based estimate, not a deployment result.

## Slide 23
BEFORE A STRONGER CLAIM
XtraFlow
Smarter signals should burn less fuel.
01
Count the junction
Replace the assumed flows with observed demand before quoting a site.
02
Film the queue
YOLO overlays are a feasibility demo. Replace assumed detector-error with labeled site video.
03
Score the corridor
Quote a grid result only from results/grid_results.json after a successful sweep.
This deck: 8 controllers · 5 test seeds (1–5) · oracle detector unless camera mode is on. · YOLO demo included
github.com/couder-04/XtraFlow
Simulation-based estimate; assumed traffic mix
XtraFlow · Simulation-based estimate
23
Notes: Close on the three conditions. Demo order was: SUMO side-by-side, YOLO story, optional overlays. Do not end on the annual litre range. The headline comparison is in results/headlines.json.